SEVEN D INDUSTRIES, INC.

# Patio Door Instruction to Reverse Handing

Step 1 – Remove the operable panel and set aside.

Step 2 – Remove the track located in the bottom sill of the frame.

Be careful not to damage track.

Step 3 – Invert the frame.

Step 4 – Reinstall the track.

Step 5 – Remove the metal rollers on the operable panel.

Step 6 – Invert the operable panel.

Step 7 – Reinstall the metal rollers on the panel.

Step 8 – Remove handle and mortis. Invert mortis and reinstall handle

Step 9 – Install the operable panel in the frame.

- Adjust the hardware.

If you have any questions please contact the 7D Service Department.

Phone 1-866-223-5002

Thank you,

7D Industries, Window Division.